## Slide 1: Fluids
Archimedes’ Principle
Pascal’s Law
Bernoulli’s Principle
Notes: Fluids Presentation
Archimedes’ Principle, Pascal’s Law and Bernoulli’s Principle Lesson
TeachEngineering.org

## Slide 2: Fluids and Buoyant Force
Fluids – Matter that flows (liquid and gas).
Mass density – Mass per unit volume of a substance. It is often represented by the Greek letter ρ (rho).
ρ = m
V
Buoyant force – The upward force on objects that are partially or completely submerged in fluids.

## Slide 3: Archimedes’ Principle

## Slide 4: Archimedes’ Principle
“Any object completely or partially submerged in a fluid experiences an upward force equal in magnitude to the weight of the fluid displaced by the object.”

## Slide 5: For Floating Objects
Buoyant force:
FB = Fg(displaced) = mf g
where mf = mass of fluid displaced
For floating objects:
FB = Fg (object) = mog

## Slide 6
Image source: 2008 Yupi666, Wikimedia Commons http://commons.wikimedia.org/wiki/File:Buoyancy.svg
Notes: Image source: 2008 Yupi666, Wikimedia Commons http://commons.wikimedia.org/wiki/File:Buoyancy.svg

## Slide 7
Image source: Bradley W. Carroll. Used with permission. http://physics.weber.edu/carroll/archimedes/principle.htm
Archimedes’ Principle:
The buoyant force is equal to the weight of the displaced water.
Notes: Image source: Source: Dr. Bradley W. Carroll, Department of Physics, Weber State University, http://physics.weber.edu/carroll/archimedes/principle.htm
Emailed correspondence for permission to use image (bcarroll@weber.edu)

## Slide 8
Image source: Bradley W. Carroll. Used with permission. http://physics.weber.edu/carroll/archimedes/principle.htm
ball: Displaced water weighs less than the ball
hull: Displaced water weight equals hull weight
Notes: Image source: Dr. Bradley W. Carroll, Department of Physics, Weber State University http://physics.weber.edu/carroll/archimedes/principle.htm
Author received permission to use image via email correspondence (bcarroll@weber.edu)

## Slide 9: Buoyant Force
Buoyant force is also equal to the difference between the weight of an object in air and weight of an object in fluid.
FB = Wair - Wfluid
In other words, the apparent loss in weight of a body immersed in a fluid is equal to the weight of the displaced fluid.

## Slide 10
Image source: Bill Winfield. Used with permission.
Notes: Author received written permission from Bill Winfield (winfieldchem@msn.com) to use this image.
Author originally found this image online, and when emailed Bill requesting permission to use these images, he sent me PowerPoints that he used in his classes. He said he did not authorize this media to be placed on the Internet so author did not formally cite the “angelfire” website because it is not his.
http://www.angelfire.com/nc3/pweb/lessons/archimed.htm#Table%20of%20Contents

## Slide 11: Other Relationships
Net force, Fnet is the object’s apparent weight:
Fnet = FB – Fg(object)
Fnet = (ρfVf- ρoVo) g
where: m=ρV
In solving buoyancy problems, the following derived expression is used:
Fg(object) = ρo
FB ρf

## Slide 12: Pascal’s Law

## Slide 13: Pressure
Pressure is a measure of how much force is applied over a given area.
P = F
A
units:
  1 Pa (Pascal) = 1 N/m2
  1 atm = 105 Pa

## Slide 14: Pascal’s Law
“Pressure applied to a fluid in a closed container is transmitted equally to every point of the fluid and to the walls of the container.”

## Slide 15
Pressure applied anywhere to a fluid causes a force to be transmitted equally in all directions.
Change in pressure disperses equally throughout the fluid.
Force acts at right angles to any surface in contact with the fluid.
A1 = 1 m2
F1 = 10 N
P1 = ___?
A2 = 10 m2
P2 = ____?
F2 = ____?
Image source: Bill Winfield. Used with permission.
Notes: Image used with written permission from Bill Winfield (winfieldchem@msn.com).
I originally found this image online, and when I emailed Bill requesting permission to use these images, he sent me PowerPoints that he used in his classes. He said he did not authorize this media to be placed on the Internet so I will not formally cite the “angelfire” website because it is not his.
http://www.angelfire.com/nc3/pweb/lessons/pascalp.htm
P1 exerted equally in all directions
P1 = P2
A1 < A2 so F1 < F2

## Slide 16: Bernoulli’s Principle

## Slide 17: Types of Fluid Flow
Laminar – When fluid particles move along the same smooth path. The path is called a streamline.
Turbulent – When fluid particles flow irregularly causing changes in velocity. They form eddy currents.

## Slide 18
Source: Wikimedia Commons http://commons.wikimedia.org/wiki/File:Toky.png
A
B
Notes: Which type of flow does each drawing represent? A is laminar flow; B is turbulent flow.
What are some real-world examples of each type of flow?
Image source: 2006 Dubaj, Wikimedia Commons http://commons.wikimedia.org/wiki/File:Toky.png

## Slide 19: Bernoulli’s Principle
Continuity equation:
A1v1 = A2v2
Bernoulli’s principle:
“The pressure in a fluid decreases as the fluid’s velocity increases.”
Bernoulli’s equation:
P + ½ ρv2 + ρgh = constant

## Slide 20
Bernoulli’s equation at different points in a horizontal pipe:
P1 + ½ρv12 = P2 + ½ρv22
Image source: 2013 Emily Sappington, University of Houston
Point 1
Point 2
Point 3
Notes: Image source: 2013 Emily Sappington, University of Houston using Microsoft PowerPoint
Image is not perfect, but it should be interpreted as a horizontal pipe with no variation in height

## Slide 21: Bernoulli’s Equation
Source: NASA http://www.grc.nasa.gov/WWW/k-12/airplane/bern.html
Notes: Image source: NASA http://www.grc.nasa.gov/WWW/k-12/airplane/bern.html

## Slide 22
Bernoulli’s equation at two different points of varying height
P1 + ½ρv12 + ρgh1 = P2 + ½ρv22 + ρgh2
Source: http://commons.wikimedia.org/wiki/File:BernoullisLawDerivationDiagram.svg
Notes: Image source: 2007 MannyMax, Wikimedia Commons http://commons.wikimedia.org/wiki/File:BernoullisLawDerivationDiagram.svg