CALCULATION OF MEAN RAINFALL AND PRECIPITATION GRADIENT (LAPSE RATE)  IN A CATCHMENT

In the following figure it is depicted for a catchment, Α: Thiessen polygons of rain stations along with their annual means (in mm), and Β: topographic map of the basin, its equal elevation lines (100 m) and the surface area between these lines.

In the following table the elevations (altitude) of the stations are given along with their percentage of influence over the basin .

| STATION | ALTITUDE (m) | % INFLUENCE |
| --- | --- | --- |
| (1) | (2) | (3) |
| Α | 27 | 1 |
| Β | 260 | 19 |
| Γ | 254 | 18 |
| Δ | 400 | 19 |
| Ε | 321 | 3 |
| ΣΤ | 390 | 15 |
| Ζ | 500 | 13 |
| Η | 490 | 12 |

YOU ARE ASKED TO

- Calculate the mean annual precipitation falling on the basin hs , using Thiessen polygons. Using this value find the volume of rain water that the basin receives yearly.

- Calculate the precipitation gradient and the basin’s mean elevation.

- Correct the mean annual rainfall for the precipitation gradient [if Ζs, Ζb is the mean elevation of the stations and of the basin respectively, then the corrected value will be h's = hs +β(Ζb-Ζs) where β is the precipitation gradient and hs is the annual precipitation amount.

FIND RAINFALL GRADIENT